## Slide 1: Evaluation of well tests using radial composite model and Dietz shape factor
Hana Baarová
Technical University in Liberec, Czech Republic

## Slide 2
Introduction
    Purpose of well testing
2. Radial Homogeneous Flow Model
Assumptions
Log-log diagnostic plot
Semi log diagnostic plot
Methods to obtain permeability (k), transmissivity (kh) and total skin
3. Radial Composite Flow Model
Scheme and assumptions
Acidization, gas fingering, moving water front
Log-log diagnostic plot
Semi log diagnostic plot
4. Dietz Correction Shape Factor
Assumptions
Cartesian plot – irregular drainage area, position of the well
Improvement in deliverability calculation
5. Conclusions

## Slide 3
1. Introduction - Well testing workflow
Pressure transient analysis data (isochronal pumping test)
Transient data (build-ups)
Early time data (ETD) - wellbore storage coefficient
Middle time data (MTD) – flow model to get permeability (k) and total skin (St)
Late time data (LTD) – boundary model to estimate boundary condition
Deliverability – semi theoretical derivation of absolute open flow potential (AOF)
Flowing periods (drawdowns)
non-Darcy skin analysis - true skin (S) and rate-dependent skin (Sd)
Deliverability - LIT analysis to get AOF
www.goexpro.com
ETD
MTD
LTD
Flow model
Boundary model
Log-log diagnostic plot
Test overview

## Slide 4
Wellbore storage effect
Decay of wellbore storage effect
Radial homogeneous flow regime
Heterogeneity?
2. Radial Homogeneous Flow Model
  Cylindrical homogeneous reservoir with well situated in the middle
Results
For the layer: k, kh, pi
For the well: s, Cs, Cd
www.fekete.com
Log-log plot of the last buildup
Semi log plot(Radial flow plot) of the last buildup
Slope of the straight line m
Lower k
Zero slope line
Test overview
Last buidup

## Slide 5
Distance to the radial discontinuity
3. Radial Composite Flow Model
Inner and outer region
Due to acidization
Change in gas saturation: gas fingering , moving water front
Steam front, CO2 miscible flooding front
Inner zone radial flow
Outer zone radial flow
Mobility Ratio
Storativity Ratio
Decrease in transmissivity
www.siam.org
www.fekete.com
(Not a double slope)
Short duration of WBS
Mobility ratio, Pseudoradial skin, Distance Lrad
Lrad

## Slide 6
4. Dietz Correction Shape Factor CA
Layer parameter, default value 31.62
Accounts for the drainage area shape and the well position
Better calculation of AOF transient, closed system
Improved AOF Trans
153 840 m3/h
AOF Trans 165 063 m/h3
AOF Lit 154 998 m3/h
Default CA = 31.62
CA = 2.3473
CA estimated from the Cartesian plot of the extended drawdown

## Slide 7
5. Conclusions
Well showing such a change in transmissivity in log-log plot
Radial composite model helpful (M, Lrad, ω, k2)
Acidization
Gas fingering effect
Moving water front
AOF´s from transient flow and drawdown´s not coherent
Irregular drainage area shape
Dietz shape factor for closed system
(low permeable wells only)
Inner zone radial flow
Outer zone radial flow

## Slide 8
Thank you for your attention